## Slide 1: Use of an MPLS LSE as an Ancillary Data Pointer draft-bryant-mpls-aux-data-pointer-00
Stewart Bryant (sb@stewartbryant.com),
Alexander Clemm (ludwig@clemm.org),
Toerless Eckert (tte@cs.fau.de)

## Slide 2: Background / Motivation

## Slide 3: Problem Statement
Certain use cases benefit from ancillary data processed/accessed as part of a forwarding decision
Problem : How to add information to MPLS packets in a way that is:
  Suitable for efficient high speed forwarding.
  Easy for the more modern existing hw to add the feature.
  Backwards compatible in terms of basic forwarding with legacy hw

## Slide 4: Approaches Proposed So Far
The approaches that have been proposed so far* rely on the forwarder:
  Finding out if the there is applicable ancillary data below BoS
  Deducing which of the ancillary data applies to this hop
Some methods make it easier to deduce if there is data, but not where the data is.
None of the proposed methods deal well with case of ancillary data that is different at different hops.
This approach builds on the observation in draft-kompella-mpls-mspl4fa that if an LSE is not ToS the TC and TTL bits are not used.
  * Except draft-stein-srtsn which puts the information in the stack

## Slide 5: Concept / Vision
Basic idea and possible extensions/variations

## Slide 6: Core Idea
Use the “spare” non-ToS fields as a pointer to the ancillary data applicable at this hop.
Semantic: “Process as described by L1, using the information pointed to by L2”
Forwards normally when L2 not a pointer or when LSR does not understand the pointer mechanism
ToS
L1
Pointer
L2
BoS
Ln
Ancillary Data

## Slide 7: Advantages
Ability to find the ancillary data without reading the whole of the stack
  Speculative processing can be expensive
Ability to specify which ancillary data is applicable applicable to which forwarding label
Simplifies packet parser as no deduction or discursion needed
Inherently general and extensible.

## Slide 8: Special Purpose Label
Assumption: pointer will an SPL of some sort.
Could make ToS indicate pointer follows, BUT that means
  We need to change the FEC of the ToS label
  We no longer have legacy compatibility
  We will need more labels in the global label table.
    Increased cost of distribution and management
    Some LSRs (particularly PE LSRs) are already saturating the global label table.
We investigate another approach later in draft.

## Slide 9: Pointer LSE
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label | Flg |S| Pointer |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Label (SPL) Triggers behaviour
Pointer to Anc. Data
Flags, e.g. octet pointer or LW pointer

## Slide 10: Single Pointer From Multiple LSEs
ToS
L1
Pointer
L2
BoS
L4
Ancillary Data
ToS in waiting
Pointer
L3
BoS
L4
Ancillary Data
New ToS
Pointer
L3
Pop ToS
Applicable to any label stack
Particularly applicable to SR
BUT
Not efficient in use of stack space to duplicate pointers

## Slide 11: A More Efficient Approach
ToS
L1
Pointer
L2
BoS
Ancillary Data
ToS in waiting
L3
Pop ToS
Use an in-stack move (swap)
More efficient in stack space
More complex than simple Pop
Need to correct pointer – subtract 4 bytes
Problem – how to know when to stop propagating the pointer LSE?
  “TTL” in pointer ?
  Bit in L3 ?
  FEC of L3 ?
  Pointer pop SPL?
Pointer
L3
BoS
Ancillary Data
New ToS
L2

## Slide 12: Multiple Pointers
ToS
L1
Pointer 1
L2
BoS
L4
Ancillary Data
Pointer 2
L3
There are times when multiple pointers are needed, for example iOAM and LBF
L1, L2 and L3 are a group of pointers for pop and “in-stack swap” operations
The semantic is “Process as described by L1, using the information pointed to by L2 and L3”

## Slide 13: Multiple Pointers cont
ToS
L1
Pointer 1
L2
Pointer 3
L4
Ancillary Data
Pointer 2
L3
Pointer 2
ToS in waiting
Pointer groups can include pointers to objects in common with other pointer groups and unique pointers.
L5

## Slide 14: Details
WIP – Work in Progress

## Slide 15: Disposition of Ancillary Data
Ancillary data needs to be removed before the payload is passed out of the MPLS domain.
This can be a lot more complicated that just dispose of n bytes.
Some methods:
  FEC of BoS LSE (as in PW or MPLS VPN)
  SPL at BoS
  BoS LSE can point to ancillary data that describes the disposition. This is a powerful approach.

## Slide 16: SPL or Regular Label?
SPLs are in short supply
ESPLs need twice the stack space
Could we use a regular label as a pointer label?
We are not talking global labels here we are talking of a small number of network wide agreed labels to be specially recognized by the forwarder.
We do not need a common label block in the normal sense (as needed by SR) since these labels will not appear in the FIB.
We will have to modify the label manager in LSRs that could have these labels in the FIB to exclude these labels. That is work but should not be “hard”.
Applicable to pointers and other types of indicator label.

## Slide 17: Ancillary vs Auxiliary vs Metadata
Metadata(sic): data whose purpose is to describe and give information about other data.
  Not really what is happening
Auxiliary: Helpful, assistant, affording aid, rendering assistance, giving support or succour(sic).
  Sounds better suited to our use of the data
Ancillary: Designating activities and services that provide essential support to the functioning of a central service or industry
  Sounds like we are doing
Source Oxford English Dictionary

## Slide 18: Questions