## Slide 1: Preferred Path Loop-Free Alternate (pLFA) IETF 105 draft-bryant-rtgwg-plfa-00
stewart.bryant@gmail.com
Uma Chunduri (uchundur@futurewei.com)
Toerless Eckert (tte+ietf@cs.fau.de)
Futurewei Technologies Inc

## Slide 2: PPR Overview
PPR provides a method of injecting paths into link-state IGPs.
In the data plane the packet is mapped to its intended path by the PPR-ID.
PPR-ID is a *single* identifier in the packet.
The format of the PPR-ID is data-plane specific (IPv6 addr, IPv4 addr, MPLS label, MAC Addr).
PPR Interop at IETF Hackathon July 2019
A
C
B
D
PPR-ID=d
PPR-ID
B
C
A
D
See draft-chunduri-lsr-isis-preferred-path-routing for encoding detail
Control plane
Data plane
(packet)

## Slide 3: Simple Link Repair
c’
[A]—-[B]--//--[C]---[D]
| |
[E]-[F]-—[G]
PPR-ID=c’
Path from B = E->F->G->C
Note this can be an arbitrary policy derived path
PLR=B
B encaps packet to c’ next hop = E via link B->E
[A]—-[B]--//--[C]---[D]
| |
[E]-[F]-—[G]
f’
Could release in Q –space
PPR-ID=f’
Path from B = E->F
PLR=B
B encaps packet to f’ next hop = E via link B->E
Q-space WRT B->C
failure
After repair, if base network:
  IP, SRv6 or MACinMAC - Simple
  MPLS classic – usual next hop label problem
  MPLS-SR – label correction easy

## Slide 4: Node Repair
Repair S-E
+----------------+
| |
| Repair S-S s1'|
|+---------->[S1]|
|| | /
|| | /
|| |/e' s2'
----->[S]----//-----[E]---------[S2]
|| | ^
|| | |
||Repair S-S3 | |
|+---------->[S3] |
| s3' |
+-------------------------+
Repair S-S2
Treat as k-1 separate failures repairing to each next-next hop.
Also repair to E in case it was only a link failure.
Each of the k repair paths for PLR (S) can follow required policy of the traffic type being repaired.
Can have multiple repairs if required by policy

## Slide 5: Traffic Engineered Repair
Primary path is A->B->C->D and is traffic engineered
Backup path is A->E->F->G->D and is also traffic engineered
TE connectors provided from B and C to TE repair path.
If A->B, or B->C or C->D fails single TE path can be used for repair
d'
A-??-B--??--C--??-D
| | | |
E----F------G-----+
Need TE backup paths because:
Critical SLA traffic must use FRR with same SLA as primary: ( 5G uRLLC or mIOT slices)
High b/w traffic carried on TE paths must not saturate best effort shortest-path-LFA-path/shortest-path-post-convergent-LFA-path.

## Slide 6: PPR Graphs
Described in draft-ce-lsr-ppr-graph
TLVs describe graph as a series of lists of paths
Any node may be a source
A source node is annotated with the S bit
In pLFA there is one destination which has the D bit set.
The destination has a PPR-ID associated with it.

## Slide 7: Simple Repair Graph
d'
A-??-B--??--C--??-D
| | | |
E----F------G-----+
Primary path is A->B->C->D
Backup path is A->E->F->G->D + B->F + C->G
If A->B, or B->C or C->D fails single pLFA path can be used for repair
We have seen this topology before
The key difference is that the repair is described in a single graph
Graph:
  PPR-ID=d’
  A(s)->E->F->G->D(d bit)
  B(s)->F
  C(s)->G

## Slide 8: A 2-Connected Network
[E]---[D]---| [E]<--[D]<--| [E]-->[D]---|
| | | | ^ | | |
| | | V | | V V
[R] [F] [C] r'[R] [F] [C] r''[R] [F] [C]
| | | ^ ^ ^ | |
| | | | | | V |
[A]---[B]---| [A]-->[B]---| [A]<--[B]<--|
(a) (b) (c)
a 2-connected graph Blue Tree towards R Red Tree towards
Example from RFC 7812. Path defined by PPR rather than from MRT algorithm.
Note we can define the paths through policy and have multiple repair paths each with its own PPR-ID(colour).
PPR-ID (RED)
PPR-ID (BLUE)

## Slide 9: Multiple Disjoint Graphs (2)
[E]<--[D]<--| [J]
| ^ | |
V | | |
[R] [F] [C]<--[G] |
r’ ^ ^ ^ |
| | | V
[A]<--[B]<--| |---[H]
[E]---[D]---| |---[J]
| | | | |
| | | | |
[R] [F] [C]---[G] |
| | | | |
| | | | |
[A]---[B]---| |---[H]
[E]-->[D]---| |---[J]
| | | ^
r’’ V V V |
[R] [F] [C]<--[G] |
^ | | |
| V | |
[A]<--[B]<--| [H]
From RFC 7812 (Fig 2)
Single Point of failure inevitable with this topology
No restriction to a single repair topology/policy
SPF
SPF

## Slide 10: Centralized and Decentralized Approaches
pLFA can support both centralized and decentralized computation of the repair path.
Any node can inject the PPR path either:
  For itself as the PLR calculating its own repair paths
  On behalf of an SDN controller managing the repair paths
Multiple nodes can inject the repair for redundancy and the duplicate will be eliminated by the IGP flooding process.
With centralized computation *any* algorithm can be used to compute *any* path or graph - e.g. bespoke dis-joint path or lossless or low path.
pLFA is independent of any other FRR approach and may be run concurrently with it.

## Slide 11: Multiple Data Planes
pLFA is applicable to multiple data-planes:
  MPLS
  MPLS-SR
  IPv6
  SRv6
  IPv4
  Ethernet
Indeed with any data plane in which the topology is known to an entity capable of computing the repair paths
It requires no additional data plane services beyond encapsulating and decapsulating the packet at the PLR and the Repair Target.

## Slide 12: Advantages
Supports any data plane type.
The control protocol is just the IGP in use.
Any repair can be constructed with a single level of packet encapsulation with no need for midpoint identifiers.
The repair can be constructed to conform to any required policy.
  Post convergence path
  TE path
  Policy of the repaired traffic
Consistency and loop checking is easy.

## Slide 13: .. and in the next episode
There is a lot to add in the next instalment
There is some IPR, which we will declare as soon as we can.
Finally:
Questions?